## Slide 1
Effects of CG on
Aircraft Flight
Characteristics

## Slide 2: Introduction
Definition of the CG
How is the CG of an aircraft calculated?
The effects on flight characteristics
The importance and risk mitigation in flight tests
Midwest Flight 5481 case study

## Slide 3: Definition and Calculation
What is center of gravity (CG)?
Why is it important?
It is the point about which an aircraft would balance if it were possible to suspend it at that point (FAA).
An airplane in flight can be manuevered by the pilot using the aerodynamic control surfaces, the elevator, rudder or ailerons.
The force changes on those surface produce rotation around the CG.

## Slide 5: The Effects on Flight Characteristics
Effects of Forward CG:
Higher due to the following formula:
Since W gets higher due to the increasing downforce on the elevator, increases.
The efficiency is lower due to the increasing need for lift and resulting increase in the induced drag (Also due to the higher trim drag).

## Slide 6: The Effects on Flight Characteristics
Effects of Forward CG:
A higher elevator authority due to the increasing moment arm.
The stall recovery is easier since the nose has a natural tendency to pitch down and there is a higher elevator authority.
Increase in the required downforce on the elevator demands a greater elevator deflection and higher control forces, so the aircraft becomes more stable but responds more slowly to pitch commands.

## Slide 7: The Effects on Flight Characteristics
Effects of Aft CG:
Lower due to having a lower downforce.
More efficient due to needing a lower lift and having a lower induced drag.
A lower elevator authority due to a shorter moment arm.
The stall recovery is harder since there is a tendency to perform a backflip and it has a low elevator authority.
Since the required downforce is lower, the aircraft is more responsive to the inputs and more agile while it is less stable.
Irreversible control systems are used to prevent backflip tendencies and mitigate the risk associated with instability.

## Slide 8: Risk Mitigation in Flight Tests
Case Study: Stall Demo of a L-29 Aircraft
 | Catastrophic | Major | Moderate | Minor | Negligible
Frequent |  |  |  |  | 
Probable |  |  |  |  | 
Occasional | X |  |  |  | 
Remote |  |  |  |  | 
Improbable |  | X |  |  | 
Risk assesment:
*Risk = Severity x Probability
(ITPS)

## Slide 9: Risk Mitigation in Flight Tests
Hazard Description:
Causes:
Effects:
Post stall gyration and fail to recover.
Aircraft out of desired conditions (CG).
Incorrect recovery technique after stall.
Aircraft impacting on the ground
Loss of aircraft and death of aircrew.
(ITPS)

## Slide 10: Risk Mitigation in Flight Tests
Minimizing Procedures:
Stall testing at minimum 5000ft AGL.
Tests will be done at idle power, wings level.
Forward CG points will precede aft CG.
Lateral fuel will be balanced.
Spin recovery procedures will be reviewed.
Corrective Actions:
Bailout if aircraft is not controlled at 1,500 ft AGL.
(ITPS)

## Slide 11: Case Study: Midwest Flight 5481
Key Facts:
Flight : Air Midwest 5481 operating under the provisions of 14 Code of Federal Regulations Part 121 on an instrument flight rules flight plan.
Aircraft : Beechcraft 1900D, N233YV
Date : January 8, 2003
Departure: Charlotte-Douglas International Airport
Event: Loss of pitch control immediatly after takeoff.
Outcome: 21 fatatlites (2 crew, 19 passengers). The aircraft was destroyed.
(NTSB)

## Slide 12: Case Study: Midwest Flight 5481
The accident was the result of two critical, unrelated errors that aligned perfectly. A maintenance error created a hidden limitation in the aircraft’s control system. An operational error placed the aircraft in a condition where that exact limitation became fatal.

## Slide 13: Case Study: Midwest Flight 5481
(NTSB)

## Slide 14: Case Study: Midwest Flight 5481
(NTSB)
The operator used outdated FAA standart average weights.
This flight occurred in winter, with passengers wearing heavy clothing and carrying unusually heavy personal bags.
The spare wheel in the aft baggage area was not included on the load sheet.
The baggage compartment on the Beech 1900D is located near the tail.
Passengers were expected to be distributed longitudinally, but most sat in the rear rows.

## Slide 15: Case Study: Midwest Flight 5481
(NTSB)
In simulation, the aircraft required approximately 9° of nose-down elevator to counteract its aft CG condition.
Due to the rigging error, the elevator could only generate about 7° of effective nose-down travel, making the aircraft unrecoverable.

## Slide 16: Thank you.

## Slide 17: References
[1] Federal Aviation Administration, Pilot’s Handbook of Aeronautical Knowledge, Ch. 10, “Weight and Balance,” FAA-H-8083-25B, 2016. [Online]. Available: https://www.faa.gov/sites/faa.gov/files/12_phak_ch10.pdf
[2] NASA Glenn Research Center, “Center of Gravity and Stability,” Virtual Aero – Bottle Rocket. [Online]. Available: https://www.grc.nasa.gov/www/k-12/VirtualAero/BottleRocket/airplane/acg.html
[3] J. D. Anderson, Introduction to Flight, 8th ed. New York, NY, USA: McGraw-Hill Education, 2015.
[4] National Transportation Safety Board, Aircraft Accident Report: Loss of Pitch Control on Air Midwest Flight 5481, Report No. AAR-04/01, 2004. [Online]. Available: https://www.ntsb.gov/investigations/AccidentReports/Reports/AAR0401.pdf